Table of Contents

1 All-glass balustrade	2

Bohle AG
Dieselstraße 10
42781 Haan
Germany
Phone: 0049212955680
info@bohle.de
www.bohle.com

| 1 | All-glass balustrades |
| --- | --- |

| 1. 1 | 0 |  |  | 0.00 EUR | 0.00 EUR |
| --- | --- | --- | --- | --- | --- |

VetroMount top mount
Manufacturer specifications:
Bohle AG
Dieselstraße 10
42781 Haan
Germany
Phone: +49212955680
Email.: info@bohle.de


1.0 System Description

Bohle, modular VetroMount all-glass balustrade system for top mount, consisting of installation profile, edge protection, glass and accessories.
The VetroMount system is suitable both for interior and exterior applications and comes with an anodised layer of 25 µm.  

The balustrade heights depend on the applicable local building regulations and usually amount to at least 90 cm, 100 cm or 110 cm on top of the finished covering, depending on fall height.

The distance of vertical, diagonal or horizontal cladding profiles to each other and their distance to the floor, the wall or the floor front edge is not uniformly regulated and must therefore be requested from the responsible building authority.

Certification: General Building Inspection Test Certificate as per DIN 18008-4
Static proof: Tested type-statics for rail and wind load


Technical description, quality characteristics

Modular balustrade system, impact resistant and non-slip, permanently UV stable and dimensionally stable, quick and simple mounting, no welding required.
The glass is installed without drill holes and can be replaced easily in case of breakage
LED strip can be optionally integrated into the glass bearing

() Rail load: 1.0 kN/m (public area)
() Rail load 0.5 kN/m (private area)

1.1 Profile for mounting on concrete floor 
- Profile for 2500 mm, anodised aluminium E6/C0 ..........running metres
- Profile for 5000 mm, anodised aluminium E6/C0 ..........running metres

1.2 Glass bearing and rubber set for glass thicknesses between 12.76 mm and 21.52 mm for fixing the glass 
Glass thickness: ........................................mm    =   ..........running metres
* Glass thickness depending on balustrade height, overload and use or according to static requirements

1.3 Cover profile:
Top cover profile E6/C0 .............running metres (important: can be used on both sides)
Top cover profile E4/C31 .............running metres (important: can be used on both sides)
Lateral cover profile E6/C0.............running metres (important: can be used on both sides)
Lateral cover profile E4/C31.............running metres (important: can be used on both sides)
Complete cover profile E6/C0.............running metres (important: for use on the fall side)
Complete cover profile E4/C31.............running metres (important: for use on the fall side)

1.4 Glass profile handrail:
- U profile .......running metres

- Stainless steel handrail, square ..........running metres
- Stainless steel handrail, round Ø 42.4 mm.......running metres
         - Handrail cover cap ....piece(s)
         - Rubber profile suitable for ........mm glass.........running metres
         - Connector, 90°.....piece(s)
         - Wall connectors........piece(s) (connected handrail)
         - Connector, straight......piece(s)


1.5 Accessories:
- End caps, anodised aluminium E6/C0 or E4/C31  ......piece(s)
       - With cover profile.....piece(s)
       - Without cover profile .....piece(s) 
       - For staircase with cover profile ...piece(s)

- Glass stopper for staircase mounting .......piece(s)
- Connecting pins...........piece(s)
- Mounting aid.............piece(s)
- Mounting hardware 
Hilti HUS3-H. (interior)....for running metres.........box with 50 pieces
Hilti HUS-HR...(exterior)....for running metres.........box with 25 pieces


Quantity: ................................ Unit: Unit price per piece: .................................. Lump sum price: ..................................

|  | Total amount: 1 |  |
| --- | --- | --- |
|  | All-glass balustrades | 0.00 EUR |

Price calculation

______________________________________________________________________________________

| Ordinal number | Short text | Amount |
| --- | --- | --- |

______________________________________________________________________________________

| 1 | All-glass balustrades | 0.00 EUR |
| --- | --- | --- |

______________________________________________________________________________________

|  | Total amount: | .......................... |
| --- | --- | --- |

______________________________________________________________________________________

| PRICE CALCULATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Tender amount without surcharge/discount: | .......................... |
|  | Surcharge/discount (0.00 %) | .......................... |
|  | Quote amount (net): | .......................... |
|  | Plus VAT (......... %) | .......................... |
|  | Quote amount (gross): | .......................... |
|  | (Place) |  |  |  |  |  |  |  |  |  |  |  |  | (Date) |  |  |  |  |  |  |  |  |  |  | (Legally valid signature) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |